## Slide 1: Introduction to Tracheo-esophageal Speech
Janis H. Deane, M.Ed.,CCC-SLP
Director, Speech-Language Pathology
Clinical Center for Voice and Swallowing
UT Southwestern Medical Center

## Slide 2: Total Laryngectomy
Three primary means of communication:
  Electrolarynx
  Esophageal speech
  Tracheo-esophageal speech

## Slide 3: Tracheo-esophageal Speech
Possible via a surgically created fistula in the wall separating the trachea and esophagus.
A one-way valve is placed in the TE tract allowing air to be shunted from the lungs into the esophagus, thus causing vibration of the PE segment.

## Slide 4: Tracheo-esophageal Speech
Advantage – a more natural sounding speech option, typically easy for patients to learn.
Disadvantage – expense and upkeep of prosthesis; initially, one-handed communicator.

## Slide 6: Timing of TE Puncture
Primary TEP – performed at the time of total laryngectomy with or without placement of a prosthesis
Secondary TEP – puncture created any time after the initial surgery

## Slide 7: Primary TE Puncture
In some hospitals, patients will have a feeding tube, a white catheter, or a red rubber catheter in the TE tract.
In some facilities, TE prosthesis is placed at time of surgery; patient then fed through NG tube or PEG if present.

## Slide 8: Secondary TE Puncture
In many facilities, a prosthesis is placed during the secondary puncture procedure by the surgeon.
In some facilities, patients have a place holder in the TE tract and the prosthesis is placed by the SLP.

## Slide 9: Secondary TE Puncture: Clinical Considerations
Esophageal integrity – Air insufflation test - Does the PE segment vibrate, can the patient attain TE speech

## Slide 10: Secondary TE Puncture: Clinical Considerations
Swallowing function – MBS study to ensure passage of foods and liquids past the TE puncture site.

## Slide 11: Secondary TE Puncture: Clinical Considerations
Tissue integrity – is patient prone to development of fistulas? Have they proven that they can heal?

## Slide 12: Initial Placement of Prosthesis
Feeding tube/catheter is removed from the TE tract
TE tract is dilated to 18-french
TE tract is measured
Prosthesis is inserted

## Slide 13: TE Tract Placeholders/Dilators

## Slide 14: InHealth Measuring Device

## Slide 15: ATOS Measuring Device

## Slide 16: Insertion Methods

## Slide 17: Insertion of ATOS Provox NID

## Slide 18: Testing for Leaks

## Slide 19: Testing for fistulas

## Slide 20: Removal of an Indwelling TEP

## Slide 21: Initial Patient/Family Training
Insertion of a catheter into the TE tract if the prosthesis should become dislodged.
Cleaning the TE prosthesis (flushing and or brushing)
Monitoring the prosthesis for leaks, either through the valve or around the perimeter
Cleaning a laryngectomy tube if present

## Slide 22: Tracheo-esophageal Voice Prostheses

## Slide 23: Non-Indwelling Prostheses
Patients can change these at home.

## Slide 24: Indwelling Prostheses
Clinician placed

## Slide 25: Indwelling Large Flange TEPs
These prostheses are the ones we use for patients who have leakage around the prosthesis.

## Slide 26: Provox Xtraflange
Placed around the tracheal side of the prosthesis to prevent leakage around the perimeter

## Slide 27: Xtraflange in place

## Slide 28: Provox ActiValve
Designed for patients with short device life due to candida growth.
Also good for patients with inadvertent valve opening due to back pressure.

## Slide 29: Patient Supplies
Prosthesis Management

## Slide 30: Cleaning in Situ
It is recommended that the indwelling prosthesis be flushed/brushed at least twice a day.

## Slide 31: Blomsinger Accessories
Flushing device can be used with all Blomsinger prostheses.
Cleaning brush is used with the Advantage prosthesis.
Plug and Valved inserts are available.

## Slide 32: ATOS Accessories
The prosthesis can be flushed in situ by the patient or a caregiver.

## Slide 33: Stomal Occlusion for TE Speech
Finger occlusion is taught as one method for occluding the stoma for TE speech.
Use of laryngectomy tubes, laryButtons, or adhesive baseplates paired with an HME filter or freehands device.

## Slide 35: HME Filters

## Slide 36: Handsfree Options

## Slide 37: Laryngectomy Tubes

## Slide 38: HME Base Plates

## Slide 39: Peristomal Supplies
Skin-Prep and silcone glue are used to facilitate adhesion of base plates.
Remove assists with removal.

## Slide 40: Laryngectomy Tube + Base Plate

## Slide 41: ATOS LaryButton with Laryclips

## Slide 42: Clinical Considerations

## Slide 43: Device Life
The TEPs are prone to damage from yeast, biofilm, reflux. This can result in peripheral leakage or central leakage.

## Slide 44: Leakage
Central leakage – through the valve
Peripheral leakage – around the prosthesis

## Slide 45: Stoma Size
Stoma too large/too small
  If stoma is too large, patient can not finger occlude and there is often too much air pressure for stoma housings to adhere.
  If stoma is too small, difficult to place and care for a prosthesis.

## Slide 46: TE Tract
Separated “party” wall – can occur due to excessive coughing, brushing the prosthesis too aggressively (patient) swelling in the TEP area, placement of a prosthesis that is too short. It can lead to the closure of the esophageal side of the puncture.
Can be caused by the patient, a caregiver or an inexperienced clinician.
Sometimes the puncture can be restored through serial dilation of the tract.

## Slide 47: Separated Party Wall

## Slide 48: TE Tract
TE tract is too large, decreased tone.
  It is difficult to get a prosthesis to stay in place in both of these situations.
  At times, the tract will continue to enlarge due to the irritation of the prosthesis – this is a complication that has increased with re-irradiation.

## Slide 50: Tissue Issues
Granulation tissue growth around the prosthesis.

## Slide 51: TE Tract Continued
TE tract too high/too low
  It is difficult to visualize the prosthesis for removal and replacement.
  It is also difficult for the patient to flush/clean the prosthesis.
  Optimal placement – 7mm below the tracheocutaneous juncture.

## Slide 52: Untrained SLP Role
Patient safety, education of physicians, nurses, respiratory therapists, peers.
Understanding patient’s unique respiratory needs.
Understanding patient’s communication limitations and options.
Understanding patient’s swallowing abilities.
Contact primary SLP for direction.

## Slide 53: Patient/Family Involvement
If patient has a TE prosthesis, chances are good that the patient and his/her family know how to care for it.
Patient/family should be consulted prior to any intervention that can disrupt prosthesis to minimize risk of losing the puncture.

## Slide 54: Good Websites
ATOS America
InHealth Technologies
American Cancer Society
Web Whispers
International Laryngectomy Association

## Slide 55
Amy Hamilton, M.A., CCC-SLP
Janis Deane, M.Ed., CCC-SLP
Cory Atkinson, M.A., CCC-SLP
Melanie Turner,
M.A., CCC-SLP
Jacob Lofland,
M.S., CCC-SLP